## Slide 1
PRE-IDEATHON TEMPLATE
GENESIS
IDEATHON
TEAM & DOMAIN
Introduce your team and the domain you have chosen
Team Name – Optimus Prime
Team Members – G A Yuvan (CB.EN.U4ARE25014)
– Manu K (CB.EN.U4ARE25026)
– Kousik Kumar (CB.EN.U4ARE25022)
– Harshitha Kothandam Sasikumar (CB.EN.U4ARE25021)
Selected Domain – #2
Problem Statement – Thermally-Managed Solid-State Battery Module with Embedded Micro-Sensors.

## Slide 2: DOMAIN PROBLEM IN OUR WORDS
TEAM
Optimus Prime
What exactly needs to be solved?
During DC fast-charging, cells heat unevenly and hot spots form at cell interfaces and tabs, where standard cooling cannot reach in time. Most packs in the market only sense temperature at module level, so local temperature differences between cells go unnoticed until they become large. The cooling is usually applied across the pack instead of where the heat is, which wastes energy and still leaves some cells hot.
Why is it important right now?
Faster charging (150 kW and above) generates more heat, and uneven heating makes cells age at different rates, reducing the pack life. The persistent overheating that occurs also raises thermal runaway risk, which is one of the main safety concerns in EV batteries. The newer solid-state cells are still at pilot stage but have different thermal needs, so a smart cooling and sensing approach is important now.

## Slide 3: WHO IS AFFECTED?
TEAM
Optimus Prime
Target users, stakeholders, beneficiaries
Primary users / target group
EV owners and fleet operators (cabs, delivery vehicles, buses) who fast-charge frequently
EV and battery-pack manufacturers who design and validate thermal management systems
Secondary stakeholders
Charging network operators, OEM warranty and service teams, and vehicle insurers
Who benefits if the problem is solved?
Drivers and fleets: faster, safer charging and longer battery life, which lowers cost per kilometre
Manufacturers: fewer warranty claims, and a thermal design that can carry over to future solid-state packs

## Slide 4: CURRENT SITUATION & CONTEXT
TEAM
Optimus Prime
Existing scenario, background and how things work today
Existing scenario and background
Most EVs use lithium-ion packs cooled by liquid cold plates or cooling ribbons, managed by a battery management system (BMS)
Chargers of 150 kW and above are becoming common, which increases heat generation inside the pack
Relevant data or facts (if available)
Li-ion cells are commonly kept near 25–40 °C, with cell-to-cell spread ideally within a few degrees
Resistive heating scales with current squared (I²R), so doubling charge current roughly quadruples it
Current workflow, step by step
Charger supplies current → cells heat up → module-level sensors read temperature → BMS raises cooling or limits charging power

## Slide 5: KEY CHALLENGES
TEAM
Optimus Prime
Main difficulties, bottlenecks, root causes and consequences
Main difficulties and bottlenecks
Hot spots form at cell interfaces and tabs, but sensors are too sparse to see them
Cooling cannot be directed at individual cells, so the whole pack is cooled the same way
Root causes behind them
Uneven current distribution, differences in cell internal resistance, and limited heat paths between cells
Per-cell sensing adds cost, wiring and complexity, so it is usually avoided
Consequences of leaving them unsolved
Cells age unevenly and the weakest cell limits the life of the whole pack
The BMS throttles charging power as a precaution, and thermal runaway risk rises

## Slide 6: EXISTING SOLUTIONS / APPROACHES
TEAM
Optimus Prime
What is already being done, and where it falls short
Existing methods, systems or alternatives
Liquid cold plates and cooling ribbons (standard in production EVs); air cooling in older, low-power packs
Immersion cooling in dielectric fluid and research-stage fibre-optic temperature sensing (emerging)
Limitations of each
Cold plates cool uniformly with little local control; air cooling struggles at fast-charge heat loads
Immersion is heavy, costly and harder to service; fibre-optic readout equipment is expensive
The gap they leave open (Key Challenges)
No widely adopted, low-cost system links per-cell sensing to targeted cooling in real time

## Slide 7: PROBLEM INSIGHTS & OPPORTUNITY AREAS
TEAM
Optimus Prime
Resources required to solve the problem
Hardware Requirements
4–6 Li-ion cells (pouch or 21700) as a stand-in for solid-state cells, plus an enclosure and cell holders
Mini-channel cold plate (3D-printed or machined), small pump, tubing and water–glycol coolant
Thermistor/RTD sensor array, microcontroller (ESP32/Arduino), flow control, film heaters to emulate fast-charge heating
Software Requirements
CAD (SolidWorks/Fusion) and thermal/CFD simulation (ANSYS or COMSOL)
Python/MATLAB for data logging, a lumped thermal model and zone-wise control logic
Other resources (Including Human Resources)
Lab access for fabrication and testing, safety equipment, and guidance from a faculty mentor
Our team of four covering mechanical design, electronics, controls and simulation

## Slide 8: INITIAL DIRECTION & EXPECTED OUTCOME
TEAM
Optimus Prime
What Is Your Expected Outcome?
What your team intends to do
Design a scalable battery module enclosure with a mini-channel cooling plate and a per-cell temperature sensor array
Add a controller that sends more coolant to the hottest zones, built to be chemistry-agnostic so it can later host solid-state cells
What you want to improve
Cell-to-cell temperature spread and peak temperature during fast-charge-like loads
Cooling energy used, compared with uniform cooling
What successful improvement should you achieve
Initial targets (to be validated): spread within about 5 °C and peak temperature below about 40 °C
Shown first in simulation, then on a small 4–6 cell demo module